The process reading from a pipe can read blocks of data of any size, regardless of the size of blocks written by the writing process. Furthermore, the data passes through the pipe sequentially bytes are read from a pipe in exactly the order they were written. It is not possible
to randomly access the data in a pipe using lseek().

Data can travel only in one direction through a pipe. One end of the pipe is used
for writing, and the other end is used for reading.A pipe is simply a buffer maintained in kernel memory. This buffer has a maximum capacity. Once a pipe is full, further writes to the pipe block until the reader removes
some data from the pipe.

In Linux kernels before 2.6.11, the pipe capacity is the same as the system page size (e.g., 4096 bytes on x86-32); since Linux 2.6.11, the pipe capacity is 65,536 bytes.

We can use UNIX domain stream socket pairs (created using the socketpair() system call described in Section 57.5), which provide a standardized bidirectional communication mechanism that is semantically equivalent to stream pipes.

In theory, there is no reason why a pipe couldn’t operate with smaller capacities, even with a single-byte buffer. The reason for employing large buffer sizes is efficiency: each time a writer fills the pipe, the kernel must perform a context switch to allow the reader to be scheduled so that it can empty some data from the pipe. Employing a larger buffer size means that fewer context switches are required.

Closing unused pipe file descriptors
The Linux-specific call fcntl(fd, F_SETPIPE_SZ, size) changes the capacity of the pipe referred to by fd to be at least size bytes. An unprivileged process can Pipes and F I Fos 891change the pipe capacity to any value in the range from the system page size up to the value in /proc/sys/fs/pipe-max-size . The default value for pipe-max- size is 1,048,576 bytes. A privileged ( CAP_SYS_RESOURCE ) process can override this limit. When allocating space for the pipe, the kernel may round size up to some value convenient for the implementation. The fcntl(fd, F_GETPIPE_SZ) call returns the actual size allocated for the pipe.

When a pipe is created, the file descriptors used for the two ends of the pipe are the next lowest-numbered descriptors available. Since, in normal circumstances, descriptors 0, 1, and 2 are already in use for a process, some higher-numbered descriptors will be allocated for the pipe.

If u want to read or write into a pipe by using STDIN /STDOUT do the following steps
int pfd[2];
pipe(pfd);
/* Allocates (say) file descriptors 3 and 4 for pipe */
/* Other steps here, e.g., fork() */
close(STDOUT_FILENO);
dup(pfd[1]); /*allocate rec closed file descriptor*/
/* Free file descriptor 1 */
/* Duplication uses lowest free file
descriptor, i.e., fd 1 */

(or)

if (pfd[1] != STDOUT_FILENO) {
dup2(pfd[1], STDOUT_FILENO);
close(pfd[1]);
}

Pipes are unidirectional
Pipes have a limited capacity
Pipes allow communication between related processes

A pipe is a unidirectional, limited-
capacity byte stream that can be used for communication between related processes.

Msg q:
The handle used to refer to a message queue is the identifier returned by a call
to msgget(). These identifiers are not the same as the file descriptors used for
most other forms of I/O on UNIX systems.
Communication via message queues is message-oriented; that is, the reader
receives whole messages, as written by the writer. It is not possible to read part
of a message, leaving the remainder in the queue, or to read multiple messages
at a time. This contrasts with pipes, which provide an undifferentiated stream
of bytes (i.e., with pipes, the reader can read an arbitrary number of bytes at a
time, irrespective of the size of data blocks written by the writer).
In addition to containing data, each message has an integer type. Messages can
be retrieved from a queue in first-in, first-out order or retrieved by type.
each message includes an integer type field, and it is possible to select messages by
type, rather than reading them in the order in which they were written.
There are limits on the total number of message queues, the size of messages,
and the capacity of individual queues.

Shared memory:
Shared memory allows two or
more processes to share the same region (usually referred to as a segment) of physical
memory. Since a shared memory segment becomes part of a process’s user-space
memory, no kernel intervention is required for IPC. All that is required is that one
process copies data into the shared memory; that data is immediately available to
all other processes sharing the same segment. This provides fast IPC by comparison
with techniques such as pipes or message queues, where the sending process copies
data from a buffer in user space into kernel memory and the receiving process copies
in the reverse direction. (Each process also incurs the overhead of a system call to
perform the copy operation.)